## Slide 1
ORBIT ACADEMY — CISLUNAR FUNDAMENTALS
MODULE 3
Naming Orbits & TLEs
Orbits around the Earth can typically be written down in six numbers — and the Space Force publishes them routinely.
Notes: Module 3 gives orbits a language. Six numbers pin down any Keplerian orbit, and a TLE is just those numbers in a fixed-column text format. The key conceptual move is invariance: which changes reshape an orbit, and which merely turn it in space.

## Slide 2
MODULE 3 · ORBIT ACADEMY
Why you care
The catalog is a stack of TLEs. Read one, and you know where any tracked object will be… up to a certain look-ahead time.
Every tracked object
gets a two-line element set — its six-number name tag plus a timestamp.
Point the sensor
tasking runs on elements: the TLE says where to look, and when.
Elements go stale
real orbits drift off their ideal ellipse — Module 4 explains why.
Notes: This is the operator's daily reality: the public catalog is literally two-line element sets. Being able to read one — even roughly — turns a wall of digits into an orbit you can picture. Plant the seed that a TLE is only valid near its epoch; staleness is next module's story.

## Slide 3
MODULE 3 · ORBIT ACADEMY
Six numbers, one orbit
1
SIZE — semi-major axis — how big; this alone sets the period
2
SHAPE — eccentricity — circle (0) to cigar (near 1)
3
TILT — inclination — the plane's angle to the equator
4
SWIVEL — RAAN — where the plane points among the stars
5
TWIST — argument of perigee — where the low point sits on the ring
6
POSITION — anomaly — where the satellite is right now
Notes: Plain words first, jargon second: size, shape, tilt, swivel, twist, position. The first two set the ellipse, the next three orient it in space, the last says where on it the satellite is now. Students drag one slider at a time in the tool and watch which readouts respond.

## Slide 4
MODULE 3 · ORBIT ACADEMY
Reshaping vs re-orienting
Change the SIZE
the period changes
size alone sets the clock
apogee and perigee move
Swivel or twist it
period: unchanged
apogee & perigee: unchanged
same orbit — new orientation in space
Invariance is the heart of the module: turning an orbit is not the same as changing it.
Notes: The heart of Module 3: re-orienting an orbit with RAAN or argument of perigee changes nothing about its size, shape, or period. Only the semi-major axis sets the clock. This distinction pays off in Module 4, where perturbations mostly swivel orbits rather than reshape them.

## Slide 5
MODULE 3 · ORBIT ACADEMY
The TLE: an orbit in two text lines
6 + 2
the six elements, plus epoch and a drag term
orbits/day
mean motion — how a TLE encodes the size
Fixed columns, no labels — a format from the punch-card era, still the standard. A TLE describes the ideal Keplerian ellipse at one timestamp.
Notes: A TLE packs the six elements plus an epoch and a drag term into two fixed-width lines. Size hides as mean motion in orbits per day, and position as mean anomaly. Stress the epoch: a TLE is a snapshot of an ideal ellipse, correct at that moment and drifting ever after.

## Slide 6
MODULE 3 · ORBIT ACADEMY
Molniya: the magic inclination
63.4°
freezes the perigee — apogee stays parked
12 h
period; it loiters for hours over the far north
Two designer orbits from one perturbation: J2 parks Molniya’s apogee over the north — and precesses a 98.2° sun-synchronous orbit to track the Sun at +0.9856°/day, same lighting every pass.
Notes: Molniya is the showpiece real orbit: highly eccentric, 12-hour period, and inclined at exactly 63.4 degrees — the magic value that stops the perigee from drifting, so apogee stays parked over the north. It gave the Soviets hours of dwell where GEO satellites sit uselessly low on the horizon. In the worksheet students invent it themselves by trial and error — let them.

## Slide 7
MODULE 3 · ORBIT ACADEMY
What you'll do
PREDICT
call your shot first
→
TRY
run it in the simulator
→
OBSERVE
note what actually changed
Drag one element slider at a time and watch which readouts respond.
Verify the invariants: swivel and twist the orbit — period, apogee, perigee hold still.
Read your own orbit written out as a live TLE.
Invent Molniya by trial and error — then ride a sun-synchronous orbit and watch its plane track the Sun.
Notes: The tool is a six-slider laboratory; the discipline is one slider at a time. The Molniya challenge is the highlight — students who discover the 12-hour, 63.4-degree recipe themselves never forget it. Close by loading real satellites and asking why each orbit was chosen.

## Slide 8
THE ONE THING TO REMEMBER
Six numbers name any orbit —
and only the size sets the clock.
Open Worksheet 3 and keep the simulator beside it.
Notes: Size and shape make the ellipse, three angles aim it, one number places the satellite on it. Everything else — period included — follows from size alone. Worksheet 3 turns this from a claim into muscle memory.