## Slide 1
ORBIT ACADEMY — CISLUNAR FUNDAMENTALS
MODULE 1
How Orbits Work
Why satellites stay up: they are falling — sideways, fast enough to keep missing the Earth.
Notes: Welcome to Module 1, the foundation of the whole course. The single idea to land today: an orbit is falling sideways fast enough to keep missing the ground. Kill the misconception that there is no gravity in space — gravity at ISS altitude is nearly as strong as at your feet. Everything else in the course builds on this picture.

## Slide 2
MODULE 1 · ORBIT ACADEMY
Why you care
Every asset you depend on — comms, GPS, missile warning — is coasting on gravity alone.
No engines hold it up
A satellite in orbit burns nothing to stay there. Speed plus gravity set the entire path.
Physics is the map
Where a satellite can and cannot be is set by its speed — not by anyone's choice.
This is your gut feel
Modules 2–8 assume the instincts you build here: crash, circle, ellipse, escape.
Notes: Frame this as the entry ticket to space domain awareness: if you know an object's speed and position, physics tells you everywhere it can be. Ask the room why astronauts float — most will say no gravity, which is wrong; they are falling together with their ship. The simulator will do the convincing in a few minutes.

## Slide 3
MODULE 1 · ORBIT ACADEMY
Space is closer than you think
420 km
ISS altitude above the surface
~7%
of Earth's radius — it skims the paint
DC → NYC
its distance when it passes overhead
On a to-scale globe the ISS ring hugs the surface. 'Space' is an afternoon drive — straight up.
Notes: People picture the ISS halfway to the Moon; it is about 260 miles up, a DC-to-NYC hop. On a to-scale globe its ring practically touches the surface. This scale reset matters because altitude turns out to control almost everything about an orbit.

## Slide 4
MODULE 1 · ORBIT ACADEMY
Release speed sets the whole shape
1
Below ~7.6 km/s — the far side dips below the surface — it re-enters (crashes)
2
7.6 km/s — the one circular speed at 600 km — a clean, constant-height ring
3
Faster — an ellipse: your release point becomes perigee, the far side balloons out
4
10.7 km/s — escape from 600 km (11.2 from the surface) — an open path, gone for good
One knob — speed at release — picks crash, circle, ellipse, or escape.
Notes: This is the speed ladder students will climb themselves at a 600 km release point. Emphasize there is exactly one circular speed per altitude; everything slower or faster is an ellipse until you cross escape. The 'fan' exercise fires seven speeds from one point and makes the family visible at a glance.

## Slide 5
MODULE 1 · ORBIT ACADEMY
Farther out = slower
LEO — 600 km
~7.6 km/s
one lap ≈ 90 minutes
≈ 16 laps every day
GEO — 35,786 km
~3.1 km/s
one lap = 23 h 56 min
keeps pace with Earth's spin
And on any ellipse: fastest at perigee (closest), slowest at apogee (farthest).
Notes: Counter-intuitive but central: higher orbits move slower — LEO races at 7.6 km/s while GEO ambles at 3.1. On one ellipse the same rule shows up as racing through perigee and crawling at apogee. Put LEO and GEO on screen together in the sim and the difference is impossible to miss.

## Slide 6
MODULE 1 · ORBIT ACADEMY
The 24-hour trick: geostationary
35,786 km
the GEO altitude
3.1 km/s
yet it never leaves its spot
86,164 s
one sidereal day — one Earth rotation
Geosynchronous = one-day period. Geostationary = that, plus equatorial — it hangs over one point. Prograde = with Earth's spin (counter-clockwise from above the North Pole).
Notes: At exactly 35,786 km the orbital period equals one Earth rotation — 86,164 seconds, the sidereal day — so the satellite stays locked over one ground point. Distinguish geosynchronous (the period) from geostationary (period plus equatorial). Note the satellite is not parked: it is doing 3.1 km/s, precisely in step with the ground.

## Slide 7
MODULE 1 · ORBIT ACADEMY
Driving the simulator
🖱 MOUSE
drag = pan · wheel = zoom · Shift-drag = rotate
⬅ ➡ ⬆ ⬇ ARROWS
steady rotation — line up an edge-on view
, and .
time flow: slower / faster
You are a camera flying around a fixed scene — dragging does not move the Earth, it moves you. R resets the view if you get lost.
Use the ARROW KEYS to tip the view until an orbit is exactly edge-on: that is how you judge its tilt (inclination) by eye.
A LEO lap takes ~90 minutes and GEO takes a day, so , and . are not a gimmick — without time warp, most of this course is too slow to watch.
The left panel is the control board: tick boxes switch real constellations on, the three sliders set up your own object, and ◇ INJECT OBJECT launches it.

## Slide 8
MODULE 1 · ORBIT ACADEMY
What you'll do
PREDICT
call your shot first
→
TRY
run it in the simulator
→
OBSERVE
note what actually changed
Drive the simulator: pan, zoom, rotate, warp time — R resets everything.
Meet the real orbits one at a time: ISS, Starlink shells, GPS, the GEO belt.
Inject your own objects at 600 km and climb the speed ladder: crash → circle → ellipse → escape.
Fire a 7-speed fan from one point and watch a whole family of orbits bloom.
Notes: The worksheet is predict-try-observe throughout: students call their shot before every injection. Let them get fluent with the camera first — nothing they press can break the sim. The fan exercise is the payoff; make sure nobody skips it.

## Slide 9
THE ONE THING TO REMEMBER
An orbit is falling sideways fast enough to keep missing the Earth.
Open Worksheet 1 and keep the simulator beside it.
Notes: If they retain one sentence, this is it — every later module leans on it. Slower falls short, faster stretches out, much faster never comes back. Send them to Worksheet 1 with the simulator open beside it.