## Slide 1
ORBIT ACADEMY — CISLUNAR FUNDAMENTALS
MODULE 2
Angular Rates & Geosync
How fast the sky moves, why GEO holds still — and why 360 one-degree slots are contested real estate.
Notes: Module 2 shifts from 'what is an orbit' to 'what does it look like from the ground.' The two skills: thinking in angular rate rather than raw speed, and keeping straight what your reference frame is. The GEO belt gives both ideas a home.

## Slide 2
MODULE 2 · ORBIT ACADEMY
Why you care
Optical sensors don't see speed — they see angular rate. And the best ring above Earth is finite.
One ring
Every geostationary satellite shares a single circle 35,786 km over the equator.
Prized real estate
TV, weather, missile warning, relay — the belt is the backbone, and slots are negotiated.
Frames matter
'Holding still' or 'turning once a day' depends entirely on what you compare against.
Notes: Operator hook: telescopes and radars measure angles and angular rates, so a slow-looking distant object may be moving kilometers per second. The GEO belt is the most contested real estate off the planet. Frame confusion causes real tracking errors, which is why this module drills it early.

## Slide 3
MODULE 2 · ORBIT ACADEMY
The sky wheels at 15 degrees per hour
15°/hr
the sky's rotation — Earth's spin reflected
15 arcsec/s
the same rate, in sensor units
86,164 s
one full turn — the sidereal day
Fixed telescope: stars streak, a GEO satellite holds still. Sidereal drive: stars freeze, the satellite streaks. You can never freeze both.
Notes: Everything in the night sky appears to wheel at 15 degrees per hour — 15 arcseconds per second — because Earth turns. A ground-fixed telescope sees stars streak while a GEO bird sits still; a sidereal drive flips which one streaks. That trade is a preview of Module 7 on observability.

## Slide 4
MODULE 2 · ORBIT ACADEMY
The belt: 360 parking spaces
35,786 km
one altitude, one ring, over the equator
360 slots
one-degree spaces (~2° real spacing)
+300 km
the graveyard boost for retired satellites
GEO is far too high to re-enter. Dead satellites can't hold a longitude — they drift. Live ones are boosted up to the graveyard to free the slot.
Notes: Because every geostationary satellite needs the same altitude over the equator, the belt is a single circle with roughly 360 one-degree slots — finite and contested. Retirement means boosting about 300 km higher into a graveyard orbit, since re-entry from GEO is not an option. Dead sats drift along the belt, a growing debris concern.

## Slide 5
MODULE 2 · ORBIT ACADEMY
Geosynchronous vs geostationary
Geosynchronous
period = one sidereal day
any inclination allowed
tilted ⇒ its ground point traces a daily figure-8
Geostationary
same one-day period
AND over the equator (0° tilt)
hangs over one fixed spot
Tilt is the whole difference — students will inject both and watch the figure-8 appear.
Notes: Geosynchronous is only a statement about the period; geostationary adds 'equatorial.' Tilt a geosynchronous orbit and its ground point swings north and south once a day, tracing a figure-8. This is the most common vocabulary slip in the field — worth drilling.

## Slide 6
MODULE 2 · ORBIT ACADEMY
Motion always needs a reference frame
1
Versus the ground — a geostationary satellite is motionless — dishes point once, forever
2
Versus the stars — the same satellite turns once per day to keep its antenna on Earth
3
Its solar panels — must counter-rotate on their own joint to stay locked on the Sun
4
The belt is tilted — the equator sits 23.5° from the ecliptic — the tilt that gives us seasons
Notes: One satellite, two true statements: still relative to the ground, rotating once a day relative to the stars. That is why its solar panels need their own rotating joint. The 23.5-degree tilt between equator and ecliptic closes the module and seeds the geometry used later for eclipses and seasons.

## Slide 7
MODULE 2 · ORBIT ACADEMY
What you'll do
PREDICT
call your shot first
→
TRY
run it in the simulator
→
OBSERVE
note what actually changed
Inject a geostationary satellite and watch it hover over one longitude.
Tilt it into an inclined geosync orbit and watch the daily figure-8 appear.
Use the ground-telescope view: freeze the stars, then freeze the satellite — never both.
Ride along with a GEO bird: watch its panels turn, and visit the graveyard orbit.
Notes: The ground-telescope scene is the heart of the worksheet — let students toggle the sidereal drive themselves. Have them predict which way stars drift before they look. The figure-8 exercise cements geosynchronous-versus-geostationary better than any definition.

## Slide 8
THE ONE THING TO REMEMBER
Geostationary isn't parked — it's a 3.1 km/s orbit exactly in step with Earth's spin.
Open Worksheet 2 and keep the simulator beside it.
Notes: The satellite only 'hovers' because its period matches one Earth rotation over the equator. Change the frame and the same object is doing kilometers per second. Worksheet 2 makes them hold both pictures at once.