## Slide 1
ORBIT ACADEMY — CISLUNAR FUNDAMENTALS
MODULE 4
Maneuvers & Perturbations
Delta-v is the currency of spaceflight — learn to spend it wisely, and to notice when someone else is spending theirs.
Notes: Module 4 adds change to the static picture: deliberate burns and the slow push of perturbations. Two big ideas — delta-v is a finite budget, and tangential burns are efficient while radial ones are wasteful, even paradoxical. This is also where prediction starts to break down.

## Slide 2
MODULE 4 · ORBIT ACADEMY
Why you care
A satellite that maneuvers is a satellite your catalog no longer knows.
The tank is finite
Delta-v is the fuel gauge of a mission. When it's spent, the mission is over.
Burns follow rules
orbit changes are physics, not magic — you can predict what a burn can and cannot do.
Everything drifts
drag, sunlight, Earth's bulge — even quiet satellites wander off their TLEs.
Notes: The SDA framing writes itself: every TLE goes stale, and a maneuver makes it stale instantly. Understanding the cost of maneuvers tells you what an adversary can afford to do. And nature maneuvers everything for free — drag, radiation pressure, and Earth's oblateness never switch off.

## Slide 3
MODULE 4 · ORBIT ACADEMY
Spend it tangentially
1
Prograde / retrograde burns — raise or lower the FAR side of the orbit — efficient
2
Radial burns — barely change the orbit at all — mostly wasted fuel
3
The paradox — pushing straight 'up' can drop your far side into the Earth
4
Kill your sideways speed — and nothing holds you up — you fall straight in
To fight drag, burn prograde.
Prograde burn increases speed
Retrograde burn decreases speed
Radial burns push inwards or outwards
Notes: Direction matters more than effort: burns along the velocity vector change orbital energy efficiently, while radial burns do almost no useful work. The radial-burn crash is the great counter-intuitive demo — pushing up brings you down. The limit case, cancelling all tangential speed, drops the satellite straight into the planet.

## Slide 4
MODULE 4 · ORBIT ACADEMY
The two-step transfer: LEO → GEO
2,400 m/s
burn 1 — raise your apogee out to GEO
1,460 m/s
burn 2 — circularize at apogee
≈ 3,860
total, against a 4,000 m/s budget
Every big transfer is the same recipe: raise the apogee, coast, then match the circular speed there.
Notes: The Hohmann-style transfer is the workhorse: one prograde burn stretches the orbit until apogee touches GEO, a second burn at apogee circularizes. About 2,400 plus 1,460 meters per second — roughly 3,860 against a 4,000 budget, so there is little margin for sloppy flying. Students race their own strategy against this recipe in the worksheet and lose.

## Slide 5
MODULE 4 · ORBIT ACADEMY
Nature produces orbital perturbations too
1
Drag, below ~1,000 km — shrinks orbits to re-entry — and paradoxically speeds the satellite up
2
Sunlight pushes — flimsy, high area-to-mass junk gets flung around unpredictably
3
Earth's bulge (J2) — steadily swivels every orbit plane
4
Escape velocity — 11.2 km/s at the surface, 10.7 from 600 km — past it, the orbit opens forever
Notes: Perturbations are the forces beyond ideal gravity: drag ends missions below about 1,000 km, radiation pressure shoves lightweight debris, and the equatorial bulge swivels orbit planes. Give the drag paradox its moment — losing energy drops you to a lower, faster orbit. Escape velocity marks the outer edge of the bound-orbit world.

## Slide 6
MODULE 4 · ORBIT ACADEMY
A perturbation as a feature: sun-synchronous precession (rotation) keeps orbital plane locked relative to the sun.
~98°
the inclination that turns J2 into a tool
0.9856°/day
plane swivel — exactly one lap per year
The orbit crosses every target at the same local sun time — consistent lighting for imagery. And because orbits drift, custody means never looking away.
Notes: Pick about 98 degrees of inclination and J2 swivels the plane 0.9856 degrees per day — one full turn per year, keeping pace with the Sun. The result crosses every target at the same local solar time, which is why imaging satellites cluster there. Close on the operational moral: drift is universal, so tracking is a continuous activity called custody.

## Slide 7
MODULE 4 · ORBIT ACADEMY
What you'll do
PREDICT
call your shot first
→
TRY
run it in the simulator
→
OBSERVE
note what actually changed
Kill a satellite's sideways speed and watch it fall straight in.
Race the LEO→GEO challenge your own way — then fly the two-step recipe and compare fuel bills.
Watch a low orbit decay and re-enter; then boost a GEO retiree to the graveyard.
Dial in ~98° and build a sun-synchronous orbit from Earth's bulge.
Notes: The freeform LEO-to-GEO challenge comes first on purpose: students burn twice the fuel, then discover the recipe. The decay and disposal scenes connect perturbations to real end-of-life practice. Keep the delta-v tally visible — it is the module's scorekeeping.

## Slide 8
THE ONE THING TO REMEMBER
Delta-v is money. Tangential burns spend it wisely — and the drift never stops.
Open Worksheet 4 and keep the simulator beside it.
Notes: Every maneuver has a price in meters per second, and the tank never refills. Efficient missions spend along the velocity vector; nature spends against everyone continuously. That tension — budgets versus drift — is the rest of the course.