## Slide 1
ORBIT ACADEMY — CISLUNAR FUNDAMENTALS
MODULE 7
Observability
How we know where anything is up there — and why distance is brutal.
Notes: Module 7 is the payoff of the whole course: space domain awareness as a sensing problem. Three ways to see an object — radar echo, reflected sunlight, thermal glow — each with hard physical limits. The through-line is custody: knowledge decays, so you must keep looking.

## Slide 2
MODULE 7 · ORBIT ACADEMY
Why you care
Space domain awareness is a sensing problem: the catalog is only as good as your last look.
Three ways to see
bounce radar off it, catch its reflected sunlight, or sense its own heat.
Every sensor has blind spots
range, shadow, daylight, weather — know which one is lying to you.
Maneuvers reveal themselves
as 'not where the prediction said' — if you looked in time.
Notes: Everything earlier assumed we know where objects are; this module asks how. Each sensing mode fails somewhere — radar with range, optical in shadow — and an operator has to know which failure applies. Maneuver detection is simply prediction versus observation, which makes timely looks precious.

## Slide 3
MODULE 7 · ORBIT ACADEMY
Radar: range⁴ is merciless
1/range⁴
the two-way echo law
7.7 million×
weaker return from GEO than from LEO at 800 km
LEO is easy, GEO is a strain, xGEO is out of reach for most radars. But radar brings its own light: day, night, sun, or shadow.
Notes: Radar illuminates the target and catches the echo, so the signal fades as the fourth power of range — double the distance, one-sixteenth the return. A GEO target answers about 7.7 million times fainter than the same object at 800 kilometers, and cislunar ranges are hopeless for most systems. The compensation: radar works day or night, shadow or sun.

## Slide 4
MODULE 7 · ORBIT ACADEMY
Optical: seeing by headlights
1
You see reflected sunlight — like bicycles at night, visible only when a truck's headlights — the Sun — catch them
2
Earth's shadow — the satellite simply vanishes — no sunlight, no detection
3
Thermal infrared — warm objects glow in their own light, even in the dark
Optical is passive and cheap at any range — but the lighting is not yours to command.
Notes: Optical telescopes see only sunlit objects against a dark sky — the driving-at-night headlights analogy carries the whole idea. In Earth's shadow a satellite disappears mid-track, and students watch exactly that in the sim. Thermal infrared recovers some of it, since warm objects emit their own glow.

## Slide 5
MODULE 7 · ORBIT ACADEMY
What each sensor actually measures
Radar
range — directly
range-rate — directly
angles: crude
Optical
precise angles (RA / DEC)
no range at all
parallax across viewpoints recovers it
And the whole sky wheels at 15 arcsec per second — 15°/hr — so timing is part of every measurement.
Notes: The two sensor families are complementary: radar delivers range and range-rate with sloppy angles, optical delivers exquisite angles with no range. Parallax — the finger-in-front-of-alternating-eyes demo — recovers range from two viewpoints. Remind them the sky itself turns at 15 degrees per hour, so every angle comes stamped with a time.

## Slide 6
MODULE 7 · ORBIT ACADEMY
Custody, cadence, intent
1
Custody — up-to-date knowledge of an object's identity and orbit — it decays
2
Cadence — re-observe before the orbit goes stale; chaotic cislunar orbits go stale fast
3
Maneuver detection — the object is not where the prediction said — someone burned
4
The ladder — orbitology (where) → characterization (what) → intent (why)
Notes: Custody is a perishable good: sensors see a tiny patch of sky, so they are pointed using predictions, and stale predictions point at nothing. Cadence follows from how fast each orbit's forecast decays — cislunar worst of all. The ladder orders the hard questions: where it is, what it is, and only then what it is up to; each rung is harder, especially for uncooperative objects.

## Slide 7
MODULE 7 · ORBIT ACADEMY
What you'll do
PREDICT
call your shot first
→
TRY
run it in the simulator
→
OBSERVE
note what actually changed
Run the radar sim: gain lifts the noise too — only integration digs the target out.
Track a satellite into Earth's shadow and watch it vanish; recover it in thermal IR.
Do the parallax demo, then tag & fit: how few angle measurements pin down an orbit?
Detect a maneuver: compare the prediction with where the object actually shows up.
Notes: The radar scene teaches the honest lesson that amplification amplifies noise as well — integration is the real tool. Tag-and-fit is the quiet star: students discover how few angles constrain an orbit, and why streaks carry extra information. End with the maneuver-detection exercise; it ties the whole course to the operator's actual job.

## Slide 8
THE ONE THING TO REMEMBER
You only know where it WAS. Custody means looking again — on a schedule the physics sets.
Open Worksheet 7 and keep the simulator beside it.
Notes: Every catalog entry is a memory that decays at a rate the orbit's own dynamics dictate. The sensing physics — range to the fourth, sunlight, shadow — decides who can look, and the chaos decides how often they must. Worksheet 7 makes them feel both constraints.